## Slide 1
CONCENTRATION
MONITOR
Real-Time AI Attention Tracking
Raspberry Pi 5 · Coral TPU · MediaPipe Face Landmarker
OpenCV
Python
MediaPipe
Edge AI
Demo Presentation · April 2026

## Slide 2
Concentration Monitor | Real-Time AI Attention Tracking
The Problem
47%
of workers report distraction as their biggest productivity challenge
2.1×
lower output when attention is fragmented vs. deep focus states
0
objective tools available at the edge for real-time feedback without the cloud
Educators and professionals need a lightweight, privacy-preserving tool that measures attention in real time — running entirely on-device, with no cloud dependency.

## Slide 3
Concentration Monitor | Real-Time AI Attention Tracking
System Architecture
CAM
Camera (CSI / USB)
RPi5
Raspberry Pi 5 (Orchestrator)
TPU
Coral TPU (Inference Accel.)
MP
MediaPipe (478 Landmarks)
OUT
Dashboard + CSV Log
Software Stack
Python 3.11
OpenCV 4.x
MediaPipe Tasks
NumPy
PyCoral (TPU)
Fully offline · No cloud · < 100 ms latency · ~$120 total hardware cost

## Slide 4
Concentration Monitor | Real-Time AI Attention Tracking
How It Works
01
Frame Capture
Camera grabs frames at 30 fps via FrameCapture. BGR frames are forwarded to the detector pipeline.
02
Landmark Detection
MediaPipe Face Landmarker localises 478 facial key-points in normalised [0,1] coordinates per frame.
03
Metric Calculation
Five metrics computed: EAR, Gaze Deviation, Head Yaw (solvePnP), Blink Rate, and MAR / Yawn detection.
04
Concentration Score
Weighted formula combines all metrics into a 0-10 score. Temporal smoothing reduces landmark noise.
05
Dashboard & Logging
Live OpenCV overlay shows score, graphs & alerts. Every 10 s the score is appended to a CSV log file.

## Slide 5
Concentration Monitor | Real-Time AI Attention Tracking
Key Metrics
Metric
Formula
Normal Range
Behavior
Weight
EAR
Eye Aspect Ratio
(|p2-p6|+|p3-p5|)/(2×|p1-p4|)
0.15 – 0.35
Drops to ~0 on blink; low sustained → drowsiness
15%
GD
Gaze Deviation
Iris centre in eye bbox → degrees
< ±30°
±8° dead-zone, degrades score to ±38°
45%
HY
Head Yaw
solvePnP (4 landmarks) → Euler yaw
< ±35°
±8° dead-zone; penalises sideways head rotation
30%
BR
Blink Rate
EAR threshold crossings / window × 60
4 – 25/min
Calibrated to tolerate deep-focus low blink rate
10%
YWN
Yawn Detection
MAR > 0.72 for ≥75% of last 3 s
Not detected
Applies –2.5 penalty to final score
−2.5

## Slide 6
Concentration Monitor | Real-Time AI Attention Tracking
Concentration Score (0 – 10)
Score = ( 0.15 × eye_score + 0.45 × gaze_score + 0.30 × head_score + 0.10 × blink_score ) × 10 − yawn_penalty
Each sub-score is normalised to [0, 1] with a dead-zone + linear ramp. Yawn penalty = 2.5 pts.
0 – 3.9
Low Concentration
Alert triggered, recommend break
4.0 – 6.9
Moderate
Acceptable, minor distractions
7.0 – 10
High Concentration
Deep focus — optimal state
Temporal smoothing: gaze & yaw averaged over 15 frames (~0.5 s) to reduce landmark jitter.
Chart: 
| Gaze Dev. | Head Yaw | Eye EAR | Blink Rate
Weight (%) | 45 | 30 | 15 | 10

## Slide 7
Concentration Monitor | Real-Time AI Attention Tracking
Real Session Data — April 20, 2026
Chart: Score over time (0–10)
| 12:30:34 | 12:30:44 | 12:30:54 | 12:31:04 | 12:31:14 | 12:31:25 | 12:31:35 | 12:31:45 | 12:31:55 | 12:32:05
Concentration Score | 6.5 | 9 | 8 | 6.5 | 9 | 6.5 | 9 | 6.5 | 6.49 | 6.5
Average Score
7.45 / 10
Peak Score
9.00
Lowest Score
6.49
Sample Windows
10 × 10 s
Optimal Windows
5 / 10 ✓
* Blink rate = 0 in log indicates windows were shorter than a full blink cycle at 30 fps.
System logged "Optimal Concentration" across 5 of 10 windows — consistent with scores of 8–9.

## Slide 8
Concentration Monitor | Real-Time AI Attention Tracking
Live Dashboard
OpenCV Window — Concentration Monitor (live preview)
[ Face Landmarks 478 pts ]
Score:
8.5
EAR:
0.28
Gaze:
+3.2°
Yaw:
−1.1°
Blinks:
14/min
_ - ^ - _ ^ - ^ - _ Score history (5 min rolling)
Dashboard Features
Real-time landmark overlay on live video
Score & sub-metrics shown as HUD
5-minute rolling score graph
Colour-coded alerts (green/orange/red)
FPS counter in top-right corner
Press 'q' to exit cleanly
The dashboard runs locally — no browser, no server, no cloud required.

## Slide 9
Concentration Monitor | Real-Time AI Attention Tracking
Offline Log Analysis
CSV columns: timestamp · score · ear · gaze_dev · head_yaw · blink_rate · recommendation
[STATS] Score Statistics
Min / Max / Avg score; distribution across Low / Medium / High bands
[TIME] Session Duration
Automatically computed from timestamps, assuming 10 s logging interval
[ALERT] Low-Concentration Periods
Lists every timestamp where score < 4.0 — pinpoints exactly when attention dropped
[TIPS] Personalised Recommendations
Blink fatigue, gaze deviation, posture alerts generated from aggregate metric averages
Run: python analyze_logs.py logs/session_YYYYMMDD_HHMM.csv

## Slide 10
Concentration Monitor | Real-Time AI Attention Tracking
Roadmap & Next Steps
v1 — Done ✓
478-point facial landmark pipeline
EAR, Gaze, Yaw, Blink, Yawn metrics
Real-time dashboard (OpenCV)
CSV logging + offline report tool
Coral TPU with CPU fallback
v2 — Short Term
Per-user calibration wizard
REST API / MQTT score stream
Web dashboard (Flask + Chart.js)
Raspberry Pi Camera Module 3
Docker container image
v3 — Long Term
Multi-person tracking (classroom)
Emotion & stress estimation layer
Teacher / HR analytics dashboard
Mobile app companion (BLE)
Open dataset for attention research
The system is open-source and designed for easy extension by the community.

## Slide 11
Thank You
Concentration Monitor
Real-Time AI Attention Tracking on Raspberry Pi 5 + Coral TPU
>> Source: /concentration-monitor
> Run: python main.py [--no-tpu] [--fps 30]
> Analyse: python analyze_logs.py logs/*.csv
Questions?
Let's discuss!